## Slide 1
FIELD GUIDANCE
THE FIRST SECTION CONSISTING OF 3 SLIDES IS AN ELEVATOR PITCH THAT REQUIRES NO NDA
PLEASE NOTE THE CONFIDENTIALITY LOGO IN THE NEXT SECTION WHICH IS A DETAILED PRODUCT PRESENTATION

## Slide 2: AR0234CS – Product Presentation
Sep 2020

## Slide 3: AR0234 – 2MP CMOS Global Shutter Imaging Sensor
Features
1/2.6” Optical Format
1920 (H) x 1200 (V)
3.0µm Global Shutter Pixel
RGB Bayer & Mono Options
Data Plane I/F - 4-Lane MIPI or 12b Parallel
Control Plane I/F – 2-wire Serial
Less than 395mW @ 120fps, full resolution
Onboard temperature sensor
Defect Pixel Correction – Static & Dynamic
-40oC to 105oC (Tj) operating temp
0 degree, 28 degree CRA options
Bare Die & CSP Packages (Y-height 5.6mm same as AR0144)
Key System Capabilities & Benefits
Leading Global Shutter Efficiency minimizes motion artifacts
Wide rows (1920 pixels) enables Fast Read in Wide FOV Applications
Programmable & Switchable ROIs, with Statistics Engines for each ROI
Auto Black Level, Auto Exposure & Control for Adaptation to Dynamic Lighting Conditions
Trigger Mode & Strobe Controls for Precision Lighting & ISP Synchronization
AP1302 ISP supports for Easy & Short TTM Imaging System Development
Extended Operating Temp Range enables Usage in Demanding Conditions
Key Applications
Scanning
Autonomous Mobility
Machine Vision
AR/VR/MR
Retail Analytics
Access Control
Orderable Part Numbers (example : Mono 28)

## Slide 4: AR0234CS – ON Part Numbers (OPN)
Mono; CRA 0deg | Description | MOQ
AR0234CSSM00SUKA0-CP | CSP Chip Tray with Protective Film | 2100
AR0234CSSM00SUKA0-CR | CSP Chip Tray without Protective Film | 2100
AR0234CSSM00SUKA0-CP1 | CSP Chip Tray with Protective Film Low MOQ | 210
AR0234CSSM00SUD20 | Bare Die | NA
AR0234CSSM00SUKAH3-GEVB | Demo Headboard | NA
Color; CRA 0deg | Description | MOQ
AR0234CSSC00SUKA0-CP | CSP Chip Tray with Protective Film | 2100
AR0234CSSC00SUKA0-CR | CSP Chip Tray without Protective Film | 2100
AR0234CSSC00SUKA0-CP1 | CSP Chip Tray with Protective Film Low MOQ | 210
AR0234CSSC00SUD20 | Bare Die | NA
AR0234CSSC00SUKAH3-GEVB | Demo Headboard | NA
Mono; CRA 28deg | Description | MOQ
AR0234CSSM28SUKA0-CP | CSP Chip Tray with Protective Film | 2100
AR0234CSSM28SUKA0-CR | CSP Chip Tray without Protective Film | 2100
AR0234CSSM28SUKA0-CP1 | CSP Chip Tray with Protective Film Low MOQ | 210
AR0234CSSM28SUD20 | Bare Die | NA
AR0234CSSM28SUD20-RC1 | Bare Die, with Low MPQ | NA
AR0234CSSM28SUKAH3-GEVB | Demo Headboard | NA
Color; CRA 28deg | Description | MOQ
AR0234CSSC28SUKA0-CP | CSP Chip Tray with Protective Film | 2100
AR0234CSSC28SUKA0-CR | CSP Chip Tray without Protective Film | 2100
AR0234CSSC28SUKA0-CP1 | CSP Chip Tray with Protective Film Low MOQ | 210
AR0234CSSC28SUD20 | Bare Die | NA
AR0234CSSC28SUKAH3-GEVB | Demo Headboard | NA
All OPNs Fully Qualified & Shipping in Volume
Die Options – Check with Marketing for Specific Instructions
Samples
Use *-CP1 OPN; first 10 units can be free; need PO beyond 10 units
Always order in x10 units

## Slide 5: AR0234CS – Product Presentation
Sep 2020

## Slide 6: AR0234CS – 2MP CMOS Global Shutter Imaging Sensor
Features
1/2.6” optical format
1920 (H) x 1200 (V)
3.0µm Global Shutter Pixel
RGB Bayer & Mono Options
Data Plane I/F - 4-Lane MIPI or 12b Parallel
Control Plane I/F – 2-wire Serial
Less than 395mW @ 120fps, full resolution
Onboard Temperature Sensor
Defect Pixel Correction – Static & Dynamic
-40oC to 105oC (Tj) Operating Temp
0 degree, 28 degree CRA options
Bare Die & CSP Packages (Y-height 5.6mm same as AR0144)
Key System Capabilities & Benefits
Leading Global Shutter Efficiency
  Minimizes motion artifacts
Wide rows (1920 pixels)
  SingleShot Fast Read in Wide FOV Applications
Programmable & Switchable ROIs
  Statistics Engines for each ROI
Auto Black Level, Auto Exposure & Control
  Control & adaptation to dynamic lighting conditions
Trigger Mode & Strobe Controls
  Precision lighting & ISP synchronization
Supported by AP1302, ON Semiconductor ISP
  Easy development of imaging system; Short TTM
Extended Operating Temp Range
  Deployable in demanding commercial conditions

## Slide 7: Tremendous Traction in Multiple Markets/Applications
Plentiful & Growing
Machine Vision
Biometrics
Autonomous Mobility
Access Control
Autonomous Mobility
Scanning
Retail Analytics
Surveillance
Medical Devices
Access Control
Autonomous Mobility

## Slide 8: GS Sensor Family – Packing More in Smaller Size with Superior Performance
AR0234
AR0134
AR0135
AR0144
MT9V034
MT9V024
6.0
3.0
1.0
0.3
2.0
MT9V024
MT9V034
AR0134
AR0135
AR0144
AR0234
Pixel Size (μm)
Resolution (MP)
Performance (FPS)
60
120

## Slide 9: ON Semiconductor Global Shutter Sensors
Specification | AR0134 | AR0135 | AR0144 | AR0234
Optical Format | 1/3” | 1/3” | 1/4” | 1/3”
Output Resolution | 1280(H) x 960(V) | 1280(H) x 960(V) | 1280(H) x 800(V) | 1920(H) x 1200(V)
Frame Rate | 54fps | 54fps | 60fps | 120fps
Pixel | 3.75um GS | 3.75um GS | 3um GS | 3um GS
Full-Well (ke-) | 7 | 11 | 7.9 | 8.55
Dark Current e-/sec @ 60C | >2000 | <150 | 75 | 63
Global Shutter Efficiency (350nm-650nm, Mono) | 1200 | 4700 | 4300 | 4300
Power @ max fps | <400 mW; 7.40 mW/fps | <400 mW; 7.40 mW/fps | <215 mW; 3.58 mW/fps | <395 mW; 3.29 mW/fps
Output Interface | Parallel / HiSpi | Parallel / HiSpi | Parallel/MIPI 2-lane | Parallel/MIPI 4-lane
Package | 9x9 iBGA | 9x9 iBGA (Pin Compatible with AR0134) | 5.6mm x 5.6mm CSP | 9.995mm x 5.595mm CSP
Notes: Full Well Capacity: This represents the amount of charge a pixel can hold before saturating. It directly impacts the dynamic range of the sensor.
Dark Current: Is a representation of electrons being created independent of photon capture. Generally seen to be higher at higher temperature. A reduction in dark current reduces the total noise floor resulting in SNR improvement
Global Shutter Efficiency:
****************************************************************************************************************
Dynamic Range: This represents a cameras capabilities to display/reproduce the brightest & darkest portions of the image . Within one image there may be a portion that is in complete black & a portion that is complete saturated. The largest possible signal is directly proportional to the full well capacity of the pixel.
Full Well Capacity: This represents the maximum number of electrons per pixel.
Higher guarantee can have
Machine vision calculate thresholds
DR = ratio of Margin of error to the total sample size
How many distinct
Pixel gives
Dark Current: In VR, close to human skin, extremely high temp will make dark current degrades on image quality which in turn will impact machine vision algorithms in finding objects
Designer of a VR headset to keep the headset cool
Global Shutter Efficiency: Additive component that increases the margin of error

## Slide 10: AR0234CS – Seamless Xfer from AR0144
Specification | AR0144
Optical Format | 1/4”
Output Resolution | 1280(H) x 800(V)
Frame Rate | 60fps
Pixel | 3um GS
Full-Well (ke-) | 7.9
Dark Current e-/sec @ 60C | 75
Global Shutter Efficiency (350nm-650nm) | 4300
Power | <215 mW; 3.58 mW/fps
Output Interface | Parallel/MIPI 2-lane
Package | 5.6mm x 5.6mm CSP
AR0234
1/3”
1920(H) x 1200(V)
120fps
3um GS
8.55
63
4300
<395 mW; 3.29 mW/fps
Parallel/MIPI 4-lane
9.995mm x 5.595mm CSP
Same Pixels
Same Architecture
Carry Forward Pixel Perf, Tuning
Carry Forward Tuning
Same Height
Common Height across Generations
Optimized for Higher Performance, Lower Power
Notes: Full Well Capacity: This represents the amount of charge a pixel can hold before saturating. It directly impacts the dynamic range of the sensor.
Dark Current: Is a representation of electrons being created independent of photon capture. Generally seen to be higher at higher temperature. A reduction in dark current reduces the total noise floor resulting in SNR improvement
Global Shutter Efficiency:
****************************************************************************************************************
Dynamic Range: This represents a cameras capabilities to display/reproduce the brightest & darkest portions of the image . Within one image there may be a portion that is in complete black & a portion that is complete saturated. The largest possible signal is directly proportional to the full well capacity of the pixel.
Full Well Capacity: This represents the maximum number of electrons per pixel.
Higher guarantee can have
Machine vision calculate thresholds
DR = ratio of Margin of error to the total sample size
How many distinct
Pixel gives
Dark Current: In VR, close to human skin, extremely high temp will make dark current degrades on image quality which in turn will impact machine vision algorithms in finding objects
Designer of a VR headset to keep the headset cool
Global Shutter Efficiency: Additive component that increases the margin of error

## Slide 11: Operational Modes
Frame Readout Overlaps with Photodiode Exposure Time
Enables Highest Frame Rates
Frame Readout Sequential to Photodiode Exposure Time
Single Frame when Triggered; Precise Control, especially with Light Controlled Applications
Synchronization of Multiple Sensors
Frame Readout Sequential to Photodiode Exposure Time
Series of Frames when Triggered; Good Control
Master Mode
Pulse Trigger Mode
Automatic Trigger Mode
Upto 120fps MIPI
Upto 30fps Parallel
Upto 237fps 2x2 bin
Upto 60fps MIPI
Upto 30fps Parallel
Upto 120fps 2x2 bin
All metrics – 1920x1200
2x2 bin – 960x600
Upto 120fps MIPI
Upto 30fps Parallel
Upto 237fps 2x2 bin

## Slide 12: AR0234CS – Superior Image Quality due to High GSE
Measured Results of AR0234CS Pixel
Stripes behind the fan are covered well
Stripes behind the fan are clearly visible
Competition
AR0234CS
GSE – Quantifies the Pixel’s Sensitivity to Parasitic Light (PLS) Contamination
PLS   GSE   Poor Image Quality (Smears, Shading Artifacts, Leaky Images, etc.)
High GSE
Low GSE

## Slide 13: AR0234CS – Wide Horizontal Pixel Count Enables Significant Benefits
AR0234CS
1600x1300
1920 x 1200 Pixels – Delivers a True 1080p Resolution
Barcodes reaching > 6” (GS1-128)
SingleShot Fast Reads with Wide Hor. Pixel Count

## Slide 14: AR0234CS – Power Profiles
Chart: 
| 30 | 60 | 120 | 120 | 237
MM Power | 258.3607 | 309.4477 | 395.6074 | 290.6974 | 375.2188
TM Power | 252.3305 | 303.3101 | 217.9609 | 350.3411
Full Resolution
2x2 Bin (960x600)
FPS   Power 
Chart: 
| 30 | 60 | 120 | 120 | 237
MM mW/fps | 8.612 | 5.1575 | 3.2967 | 2.4225 | 1.5832
TM mW/fps | 8.411 | 5.0552 | 1.8163 | 1.4782
Power Efficiency
AR0234CS  – FPS   Power/FPS 
Trigger Mode Power < Master Mode Power
FPS
mW/FPS
FPS
mW
Requires Smaller Power Budgets, Enables Superior Camera System Performance
NOTE – FPS to mW is non-Linear due to Analog Content
Full Resolution
2x2 Bin (960x600)

## Slide 15: Spectral Characteristics

## Slide 16: CRA Curve for Lens Selection
28deg Curve

## Slide 17: Package – Small Footprint Enables Tiny Modules
Contact Your Sales/FAE if Only Dies are Needed
9.995mm
5.595mm

## Slide 18: AP1302 Companion ISP
Deployed in Millions of Imaging Systems
And Many More……
Parameter | Value
Maximum processing speed | 450 MPix/second (13MPix@30FPS)
Maximum output resolution | 4224x3156 (13 MPix)
Input | MIPI 4x1.2Gbps
Output | MIPI 4x1.2Gbps
Package | 6.5x 6.5 x 0.8(mm) VFBGA
AR0330, AR0821, AR1335, AR1820
AR0144, AR0261
AP1302 Shipping in Volume Since 2015
Host Processor
SPI Serial Flash Memory
Sensor1
Sensor2
MIPI 4x1.2G
MIPI 2x1.2G
MIPI 4x1.2G
AP1302
I2C Master
I2C Master
Sensor I/F0
Sensor I/F1
Host I/F
I2C Slave
and/or SPI Slave
(muxed with GPIOs)
SPI Master
(muxed with GPIOs)

## Slide 19: AR0234CS + AP1302 – A Powerful Combination for Camera System
Other ISPs
System Development Time
With AP1302
Months Saved !!
Sensor Tuning
Calibration
Performance Optimizations
AR0144
AP1302
Host
Transparent Switching between Sensor Modes
AR0144
Seamless Switch between Product Generations
AR0234
AR1335
AP1302
Host
Same 1302, Same Host
AP1302
Host
Same 1302, Same Host
Native
Binning
Skipping

## Slide 20: DevSuite – Comprehensive SW Eases System Level Design
Libraries
Tools
Hardware Interface
DevWare GUI

## Slide 21: AR0234CS – Full Development System Available
Provides Full Testing Capabilities
Hardware Capabilities
  Output Size
  Frame Rate
  Gain & Exposure
Software Capabilities
  Graphing
  Color Pipe
  Noise Reduction
  Image Statistics
Enables Product Evaluation before Starting Product Design
Provides Reference during Design Stage
Available for Order
AGB1N0CS-GEVK (Demo3 Board)
AR0234CSS***SUKH3-GEVB (AR0234CS Board)
AR0234CS Sensor Headboard
(comes with a default lens)
DevWare SW

## Slide 22: AR0234CS + AP1302 + DevSuite – Rapid Camera System Design
Development Hardware Kit
AGB1N0CS-GEVK (Demo3 Board)
AP1302CSSL00SMGAH3-GEVB (AP1302 Board)
AR0234CSSC00SUKH3-GEVB (AR0234CS Board)
Development Software
DevWare Base Package (SW Platform)
AP1302 SW Package (AR0234 Specific Support)
Parametrized, Modifiable Default Inputs, Customized Outputs
Configured
Calibrated
Tuned
Output
AP1302 Init File (XML)
Usable in System Design
Saves Several Months of Camera System Development
Pls contact your FAE for details on setup & use

## Slide 23: Module Support – Some Examples
Multiple AR0234 Modules
AR0234 Module
Nano | TX2 | USB3.0
Driver Support
Nvidia Jetson Camera Kit
Coming Soon !
Nvidia Jetson Camera Kit CY21
Drivers – In Works
Multiple AR0234 Modules
Complete System
Available NOW!
Nano | TX2 | Xavier
Socionext ISP MBG967 Tuned
Nvidia Jetson Camera Enabled

## Slide 24: AR0234CS – Reference Designs
Machine Vision Reference Module (MVRM)
AR0234CS + AP1302 + USB3.0 Stack
Compact, MV Camera Form Factor 26x26x13mm
Readily Deployable HW Module with USB3 Driver
More Support Coming Soon !
Driver Monitor Reference Design (Primax)
AR0234CS + QCOM QCS603
Ready to Deploy – HW + Drivers
Contact ON Sales &/or Primax !
OpenNCC Camera Reference Platform (Eyecloud)
AR0234CS + Intel VPU + OpenVINO
Rapid AI Camera based Solutions
Sensor Fusion, Object Det/Class/Rec
Intel’s AIoT PaaS Platform
Available Now !
AR0234CS
AP1302
USB3 Bridge
Check with Marketing for Additional Information

## Slide 25: Multiple ISPs Support AR0234CS
VATICS
M5S
Appro.Pho Camera Module - AR0234(Global shutter)+ISP(YUV)+AF Zoom lens(4.4X)
Others in Works!
Qualcomm – QCS603
VATICS – M5S
Nvidia – Jetson Platforms
Socionext – MBG967

## Slide 26: AR0234CS – Ordering
AR0234 CS S M 00 S U K A 0 - C P
Web Part Number
WPN
CMOS Sensor
CS = Default
Revision
S = Default
Chromaticity
CRA Angle
Operating Temp
S = Commercial
Interface
U = Multiple
Package
K = CSP
Package Options
A = Lead Free
Ship Package
C = Chip Tray
P = Protective Film
R = No PF
# Extns for Lower MOQs
Special
0 = Default

## Slide 27: AR0234CS – ON Part Numbers (OPN)
Mono; CRA 0deg | Description | MOQ
AR0234CSSM00SUKA0-CP | CSP Chip Tray with Protective Film | 2100
AR0234CSSM00SUKA0-CR | CSP Chip Tray without Protective Film | 2100
AR0234CSSM00SUKA0-CP1 | CSP Chip Tray with Protective Film Low MOQ | 210
AR0234CSSM00SUD20 | Bare Die | NA
AR0234CSSM00SUKAH3-GEVB | Demo Headboard | NA
Color; CRA 0deg | Description | MOQ
AR0234CSSC00SUKA0-CP | CSP Chip Tray with Protective Film | 2100
AR0234CSSC00SUKA0-CR | CSP Chip Tray without Protective Film | 2100
AR0234CSSC00SUKA0-CP1 | CSP Chip Tray with Protective Film Low MOQ | 210
AR0234CSSC00SUD20 | Bare Die | NA
AR0234CSSC00SUKAH3-GEVB | Demo Headboard | NA
Mono; CRA 28deg | Description | MOQ
AR0234CSSM28SUKA0-CP | CSP Chip Tray with Protective Film | 2100
AR0234CSSM28SUKA0-CR | CSP Chip Tray without Protective Film | 2100
AR0234CSSM28SUKA0-CP1 | CSP Chip Tray with Protective Film Low MOQ | 210
AR0234CSSM28SUD20 | Bare Die | NA
AR0234CSSM28SUD20-RC1 | Bare Die, with Low MPQ | NA
AR0234CSSM28SUKAH3-GEVB | Demo Headboard | NA
Color; CRA 28deg | Description | MOQ
AR0234CSSC28SUKA0-CP | CSP Chip Tray with Protective Film | 2100
AR0234CSSC28SUKA0-CR | CSP Chip Tray without Protective Film | 2100
AR0234CSSC28SUKA0-CP1 | CSP Chip Tray with Protective Film Low MOQ | 210
AR0234CSSC28SUD20 | Bare Die | NA
AR0234CSSC28SUKAH3-GEVB | Demo Headboard | NA
All OPNs Fully Qualified & Shipping in Volume
Die Options – Check with Marketing for Specific Instructions
Samples
Use *-CP1 OPN; first 10 units can be free; need PO beyond 10 units
Always order in x10 units

## Slide 28: AR0234CS – Technical Documentation
Comprehensive Set Available on Doc Management

## Slide 29: AR0234CS – Technical Documentation
AR0234CS ISG Extranet Documents Folder - https://cma.onsemi.com/PowerSolutions/cma/erFileEdit.do?folderId=1503046

## Slide 30: Details

## Slide 31: AR0234CS – Block Diagram
Incident LIght

## Slide 32: AR0234CS – Pixel Array – With Power Optimization Capabilities
Dark Pixels – Remove Thermal Noise Energy in Image Data Output
Barrier Pixels – Separators between Pixel Categories
Light Dummy Pixels – used for Color Reconstruction

## Slide 33: Good Performance, High Image Quality @ High & Low Lux
500 Lux, 1.684x Gain, 8.3ms Texp
10 Lux, 16x Gain, 26ms Texp

## Slide 34: Same High Performance @ Different Frame Rates
22 Lux, Gain 16x, Texp 16.67ms, 120 fps
22 Lux, Gain 16x, Texp 16.67ms, 60 fps

## Slide 35: Good Image Quality @ High & Low Light, Different Frame Rates
500 Lux, Gain 2x, Texp 6ms
60 fps, 2-Lane MIPI
120 fps, 4-Lane MIPI
10 Lux, Gain 50x, Texp 14.2ms
60 fps, 2-Lane MIPI
120 fps, 4-Lane MIPI

## Slide 36: Thank You!